## Slide 1: High Speed 64kb SRAM
ECE 4332 Fall 2013
Team VeryLargeScaleEngineers
Robert Costanzo
Michael Recachinas
Hector Soto

## Slide 2: Outline
Problem
Design Approach & Choices
  Circuit
  Block
  Architecture
Novelties
Layout
Simulations & Metrics
Future Work

## Slide 3: Problem
Portable Instruments Company (PICo) desires SRAM for a new mobile node
  High Speed 64kb cache, or
  2 Mb Low Power SRAM
Team VLSE’s problem:
  First priority: delay
  Seek to also minimize area, power, and energy

## Slide 4: Design Approach
Architecture Level
  Pareto Curve
    32-Blocks
Carr D., Park J., Reyno D. “A High Speed 64kb SRAM Cache in 45nm Technology” (2010)

## Slide 5: Final Schematic
Pins
Decoders
Block 0
Block 1
0
1
31

## Slide 6: Block Diagram

## Slide 7: Block Level
Transmission gates
  AND, MUXes, etc.
Notes: It’s really easy to use TX gates because
TX gates are stabler, fewer transistors, faster, stack effect

## Slide 8: Bit Cell Level
Traditional design

## Slide 9: Bit Cell Level
γ =
ISA
ISD
LDWA
WDLA
=
Icell <
γ
ISD
Icell >
γ+1
ISD
Icell >
γ+1
γ ISA
Icell < ISA
Pass Gate
PDN NMOS
All equations and images on this page are from Ding-Ming Kwai & IP Library Company

## Slide 10: Bit Cell Level
Carr D., Park J., Reyno D. “High Speed Cache” Powerpoint Presentation to PICo (2010)
Desire: small area & stable Q
Reality: only need to get below VM, don’t need to get below VT
We ended up with a cell ratio of 1.2 and Pull-up ratio of 1.11, following Carr et al.’s (2010) successful design choices as well

## Slide 11: Device Level
W/L determined by sweeping and using previously mentioned ratios
  PMOS: 180n
  NMOS: 240n
  Pass Gate: 200n
Compared to previous years, industry standard, etc.
  Short Answer: bigger

## Slide 12: Novelties
Latching Voltage Sense Amplifier
Stacked Transmission Gate Decoders

## Slide 13: Sense Amplifier
Differential
ECE410 Chapter 13 Lecture at Michigan State
Pros
Easy to implement
Dynamic
Low Power
Cons
Dynamic
Main Idea:
BL > BLB: Output = high
BL < BLB: Output = low
ΔVBL= IcellΔt / CBL

## Slide 14: Latching Voltage Sense Amplifier
Pros
~23% Faster Reads*
  Therefore, ~23% smaller ΔV
Low power
Cons
More FETs/Larger area
Ryan, J. F., & Calhoun, B. H. “Minimizing offset for latching voltage-mode sense amplifiers for sub-threshold operation” (2008)
*Based on 2011 Team 1 measurement

## Slide 15: Layout
Note: No taps are present in the layout
We attempted to optimize area as well
Clutter

## Slide 16: 6T Cell Layout
1.0675 μm
2.16 μm

## Slide 17: 2x2 Cell Layout

## Slide 18: Block Layout
60.295 μm
69.12 μm

## Slide 19: Block with Peripherals
69.63μm x 74.365μm

## Slide 20: Sense Amp
Differential Voltage Latching Sense Amplifier
Messy, Cluttered

## Slide 21: Transmission Gate
Versatile, Used in most of the peripherals
Helpful with other layouts

## Slide 22: 32b Decoder Layout

## Slide 23: 64b Decoder Layout

## Slide 24: Testbench
Simulation setup for SRAM
  Reads and Writes
To emulate conditions seen in full array:
  Recreate worst case paths
    For both inputs and outputs

## Slide 25: Simulation Results
PRECHARGE
WORDLINE
READ
WRITE
Q
QB
DATA
OUT

## Slide 26: Metrics
Metrics | Our Group | Comparison to Team XOR (2010)
Total Metric | 1.024 x 10-29 J·s2·mm2·W | Better by 882%
1 Bitcell Area | 2.3 μm2 | Worse by 130%
Total Area | 0.1657 mm2 | Worse by 22%
Total Energy | 3.0348 nJ | Worse by 20%
Read Delay | 0.54 ns | Better by 63%
Write Delay | 0.11 ns | Better by 58%
Total Delay | 0.54 ns | Better by 63%
Idle Power | .0698 W | Better by 41%

## Slide 27: Future Refinement
SKILL and OCEAN
Carr D., Park J., Reyno D. “A High Speed 64kb SRAM Cache in 45nm Technology” (2010)
Move further on the Pareto curve
Predecoding
Error Correcting Code
Vectorize signals
Ultra-thin Layout

## Slide 28
& Team XOR (2010),
Team 2 (2010),
Team 1 (2011),
and many others!
Dr. Benton Calhoun, PICo liaison
Aatmesh Shrivastava, PICo liaison
University of Virginia
Divya Akella
We also acknowledge and offer good luck to Team Innovation!
Acknowledgments

## Slide 29: Questions? ಠ_ಠ

## Slide 30: References
[All pictures are cited in their captions]
Calhoun, B., Design Principles for Digital CMOS Integrated Circuits, (March 7, 2012)
L. Hamouche and B. Allard, “Low power options for 32nm always-on SRAM architecture,” Solid State Electronics, 2011.
Mann, R., and B. Calhoun, "New category of ultra-thin notchless 6T SRAM cell layout topologies for sub-22nm", ISQED , 2011.
Rabaey, J., Chandrakasan A., Nikolic, B., Digital Integrated Circuits (2nd Edition), (Dec 24, 2002)
Rabaey, J. Digital Integrated Circuits: A Design Perspective. Prentice Hall, 2003.
Ryan, J. F., & Calhoun, B. H. Minimizing Offset for Latching Voltage Mode Sense Amplifiers for Sub-Threshold Operation. 9th International Symposium on Quality Electronic Design, 2008.
Wang, A., Calhoun, B. H., & Chandrakasan, A. P. Sub-Threshold Design for Ultra Low-Power Systems. Springer, 2006.
Previous Groups from ECE 4332 VLSI Design at University of Virginia (e.g. 2009, 2010, 2011, 2012)